Purpose:  General instructions for using the Wheaton Omnispense Plus for aliquoting out large numbers of test tube media

Materials

|  | Manufacturer | ID # |
| --- | --- | --- |
| Omnispense Plus | Wheaton |  |
| Sanisol |  |  |
| Deionized Water |  |  |

Background:

The Wheaton Omnispense Plus is an automatic dispenser that allows for the dispersion of large quantities of set volume samples.   This item is more accurate and less time consuming than manually pipeting.

General Notes:

- Make sure that the units power is switched off before using and after use.

Procedures

- Cleaning surfaces with Sanisol disinfectant.   Let the Sanisol dry or wipe the excess Sanisol off after 1 minute.

- Turn unit on using the switch on the back of the Unit.  Let the unit power up for a minimum of 5 minutes.

- Assemble all of the materials that will be needed for dispersion.   (Tubes, Media ect) plus a small container of water and a container or sink for excess fluid.

- Place the tube end containing the hose weight in your solution of Distilled water.

- Prime the tube and rinse with 50ml’s of distilled water

  - Click on sel

  - Enter 50ml under volume

  - Click on enter

  - Click on Stop

  - Make sure that the machine is set to maunul using the auto man button

  - Click on start to prime and flush the line with water.

6.0   Repeat steps 5.1 to 5.6 with the media that you will be despensing

Click setup

Pump Mode (0-1)   should be dispenser if not pres 0 pres sel

Footswitch   (0-1) should be stop if not press 0 pres sel

Backlight (0-2) should be on if not pres 1 pres sel

Rampdown (0-1) should be No if not press 0 then press sel

Beep (0-3) is operators choice  0 is silent press sel

Click on stop   display should read dispenser Auto,  press Auto Man button until the reading is Dispenser Manual

Click SEL Change volume to 50ml  click on enter

Click on stop

Click on Start this will run 50mls of fluid through the tubes to both prime the tube and rinse the tube out.

Once it is complete click on Stop twice

Calibrating the Unit

Click on Vol. CALIB

Make sure you have your entire materials ready, mostly a flask that has water in order to calibrate the machine as well as a graduated cylinder.   Slick on the start button to begin measuring.   Once the volume is close to your desired volume click on the stop button,   The  Display will ask  what the actual volume is.   Enter your volume to the closet 0.1ml.

Once you add it press enter

Set the despising parameters.

Click on AUO Man  Until the screen reads Dispenser Auto

Click on sel   enter the volume you wish to dispense

Click on sel delay time is 1 second

Click on sel P.R is 0

Click on sel   The count is the number of tubes that you wish to make

Click on sel  Pump RMP is set to max of 150

Click on sel   ramp is 0

Click on sel the motor direction is cw

Click on sel  store as 32

Click on sel  recall as 32

When volume come up again click on stop 2 times.

When you are ready to dispense move the dispenser over your tube and enter start

(On all of these will need to hit enter if changing the value selected)

Remember to add 10% more for filling the lines and what not.

Flush out the lines afterwards, with water.

Click on Sel, display should read volume, change to 50ml, sel

Delay should be 1.0 seconds pres sel

PR should read 0 pres sel  .