Purpose:  Instructions for the Operation of the Corning Stirrer, Single Position, Slow Speed Stirrer

Materials

| Corning Slow Speed Stirrer | Model Number 440812 – Single Position |  |
| --- | --- | --- |
| Two Piece Power Connection Set | Power Supply Unit DC 12v, 3.8a Dual Prong Power Cord |  |
| Log | Form 1200.08 Corning 1 Position Slow Speed Stirrer |  |

Background: The corning slow speed stirrers are designed specifically for spin flasks and for stirring tissue culture cells.   The reason these stir plates are expensive is that they have been geared down so that the fragile tissue culture cells are not sheered.   Most laboratories have other stir plates that spin at least 200rmp, which would produce a sheer force that will kill tissue culture cells.

Before operating this equipment perform a fit for use inspection.

The rotary knob on the front of the stirrer turns power “ON” and “OFF” and allows the speed to be set.  The markings on the knob indicate the approximate stirrer speed in R.P.M.

Procedure

- General handling:

1.10 Assure that the speed control knob is in the “OFF” position.  The “OFF” position is attained by turning the stirrer speed control knob counter clockwise clicking past the zero mark.

1.20 Join the stirrer lead connector to the out output lead connector for the power supply unit. Connect the power supply unit to the dual prong power cord, then insert to a power receptacle.

- Center the spinner flask with media solution and stir bar onto the surface. Check with your instructor to ensure you are using the proper stir bar size for the spinner flask being used.

- Set the speed. Speed should be slow enough to avoid a vortex.

- Fill out the log sheet.

- When stirring is complete, turn speed control knob to the “OFF” position.  Remove spinner flask.  Clean the unit accordingly.

2.10  Depress foot pedal on lower right (Door Open/Close) to open door.

2.20  On the touch screen, press ‘cycle select’.

2.30. Select appropriate cycle (1-6).

2.40  Check the specifications for the cycle as to temperature and time on screen.

2.50  Press ‘start cycle’.

2.60  Record the cycle count on the autoclave log.

2.70  Sign your initials as the operator and note cycle type and # on the log.

3.0  Procedure to open the autoclave after cycle is complete:

3.10  Depress foot pedal on lower right (Door open/close).

3.20  After the door is open, allow steam to escape before removing items.

3.30  Using hot hands or autoclave gloves, remove items from the autoclave.

3.40  Reload the autoclave or close the door when done.