Purpose:  General instructions on sanitizing hands, surfaces and small reusable materials in the GMP laboratory.

Materials

| Material | Manufacturer | Active Ingredient | ID# |
| --- | --- | --- | --- |
| Pro Quality Moisturizing Antibacterial Hand Sanitizer | Pro Pride | 62% Ethyl Alcohol | 457121 |
| Instant Hand Sanitizer | Purell | 62% Ethyl Alcohol | 482245 |
| Disinfecting Wipes Bleach Free Fresh Scent | Clorox | n-Alkyl Dimethyl Benzyl Ammonium Chloride 0.145% and N-Alkyl Ethylbenzyl Ammonium Chloride 0.145% | 897598 |
| Disinfecting Wipes | Lysol | n-Alkyl Dimethyl Benzyl Ammonium Chloride 0.28% | 897793 |
| Sani-Hands II Instant Hand Sanitizing Wipes | Nice –Pak Products, Inc. | 65.9% Alcohol | Q43884 |

Background

General Notes:

- Sanitizing typically follows general cleaning procedures SOP 200.1

- The following procedure is generally used for sanitizing hands, surfaces and small laboratory ware.

- These procedures are not meant to sterilize the materials, but in general render the materials free of chemicals or residues and microbiological contamination left by general handling or from previous procedures.

- Materials that have touched product have to have “change over” procedures performed in order to ensure that no residual product is transferred.

- In general sanitized items must be placed on sanitized surfaces.   Any sanitized items that touch unsanitized materials should be considered unsanitized and need to be sanitized before use.

Procedures

- Sanitizing hands

  - Remove a Sani-Hands II wipe from its container.

  - Then rub all the surfaces of each hand with the wipe.

  - Continue until the wetness from the sanitizer has dissipated

  - Hands should be sanitized before and after your shift as well as when entering and leaving the production rooms, or when going in-between rooms.  Hands should also be sanitized after coming into contact with soiled materials if the hands are not gloved.

- Sanitizing work surfaces

  - Fold a sanitizing wipe in half.

  - Working from left to right in a back to front motion, wipe the surface with the sanitizing wipe.   Each surface of the wipe should only be used for 2 passes back to front.   After 2 passes turn the wipe over and wipe with the back side.   After these 2 passes fold the wipe over to the inside and repeat.

  - The surface cannot be used until it is dry.

- Sanitizing small reusable laboratory ware

  - Sanitize hands

  - While transferring the laboratory ware to your previously sanitized workspace, wipe the item down (all surfaces) with a sanitizing wipe.

Define SOP:

A standard operating procedure is a set of instructions having the force of a directive, covering those features of operations that lend themselves to a definite or standardized procedure without loss of effectiveness.

Can you do  better?